## Slide 1: NSI2
Tidying Up the National Structure Inventory
Nick Lutz
Alex Ryan

## Slide 2: Overview
NSI replacement using ESRI, CoreLogic, and Microsoft data to greatly improve accuracy
We’ll answer questions you may have such as:
  Where are you getting data?
  What’s new?
  How’d that work out for you?
  When are other things happening?

## Slide 3: Data Sources
ESRI
  Non-residential structures (incl. RES4, 5, & 6)
  Location, occtype, number of employees
CoreLogic
  Residential structures (RES1, 2, and 3)
  Location, occtype, residential housing units, year built, number of stories
NCES
  Schools (EDU1 only)
  Location, occtype, teacher and student counts
Microsoft
  Structure footprints, incl. centroid location and perimeter/footprint area
CoreLogic
  Parcel locations, used to match structures to Microsoft footprints
LEHD
  Worker counts by residential location and working census block
Census
  Census block population and housing unit counts
  Structure characteristic data
FEMA/HAZUS
  FIRM Flood zone maps
  Structure characteristic data

## Slide 4: Data Sources
Layered, composite approach
  Gaps in higher resolution data filled with next best available
  Examples:
    Structures with missing Microsoft footprints placed at parcel centroid
    Missing ESRI, CoreLogic structures filled from NSI1

## Slide 5: Data Sources
Available data is used together in any combination
  Here CoreLogic structures are not available, NSI1 structures are combined with Microsoft footprints yielding high degree of geospatial accuracy

## Slide 6: Improvements over NSI1
Geospatial Location
Number of stories
Improved population assignment
Structure values
FIRM data and other added information
Better platform for future enhancements

## Slide 7: Improvements - Geospatial Location
NSI1 accurate to Census block level
  Refined by developed area layer
NSI2 adds 2 additional layers of precision, given availability:
  Parcel level (CL, ESRI)
  Structure footprint level (Microsoft)
Structure “node” precision as well as, to a lesser degree, discrete structure location precision (i.e. geospatial distribution of structure nodes by type)

## Slide 8: Improvements - Geospatial Location
NSI1 structures distributed evenly across developed areas of Census block
Structure occupancy type does not inform location
CENSUS BLOCK
RES
COM

## Slide 9: Improvements - Geospatial Location
NSI2 uses both parcels and Microsoft footprint data to refine placement
CoreLogic/ESRI parcels create structure type based placement
In multi-structure parcels structures distributed according to type
3x Com
2x Com
2x Com
1x Com
6x Res1
RES3B
RES3B
1x Com
1x Com

## Slide 10: Improvements - Geospatial Location
NSI2
NSI1

## Slide 11: Improvements - Geospatial Location
NSI1
NSI2

## Slide 12: Improvements - Geospatial Location
NSI1
Potential floodway
NSI2
Potential floodway

## Slide 13: Improvements - Number of Stories
NSI1 number of stories
  Residential – based on regional averages
  Non-residential – based on generic assumptions
NSI2 number of stories is a composite of different sources/assumptions
  Residential – based on regional avg, by year
  Non-residential – computed based on employee or other occupant counts

## Slide 14: Improvements - Number of Stories
Residential number of stories calculated similarly to NSI1, with additional use of structure year built
Chart: Number of Stories % -- West Census Region

## Slide 15: Improvements - Number of Stories
Non-residential number of stories estimated using total employees and residential units, avg sq ft per employee/unit by occupancy type
Needed minimum sq ft from this calculation converted to number of stories using perimeter
  Either from Microsoft footprints or estimated by occtype avg

## Slide 16: Improvements - Number of Stories
NSI2 approach results in variability in number of stories by structure

## Slide 17: Improvements - Number of Stories
NSI1 number of stories assigned fixed values at occtype level

## Slide 18: Improvements - Number of Stories
NSI1
NSI2
NSI1 approach does not capture meaningful geospatial variation in numbers of stories
NSI2 better captures this variability by basing estimate on structure specific characteristics
This weird space elevator thing suggests further room for improvement
(It’s not our fault though, promise)

## Slide 19: Improvements - Population Assignment
Population assignment incrementally improved over NSI1, using similar approach
  NSI2 uses working population over 65 from LEHD to refine estimates of over 65 population at non-residential structures
  NSI2 uses structure specific data (residential units/employee counts) to weight population instead of occtype level averages
  Population growth relative to 2010 Census inputs added first to areas of new development
Improved coverage
Improved distribution of over 65 population in non-residential structures
Improved geospatial distribution of working population

## Slide 20: Improvements - Population Assignment
NSI1 assumed over 65 population were equally likely to work as under 65 population

## Slide 21: Improvements - Population Assignment
NSI2 uses LEHD data on % of elderly population per Census block working to distribute over 65 workers
  Results in significantly reduced over 65 population in non-residential structures

## Slide 22: Improvements - Population Assignment
Population assignment in NSI1 done by occtype level weights

## Slide 23: Improvements - Population Assignment
NSI2 population assignment by employee counts and residential units results in more granular distribution
  Tall Office buildings absorb a lot of PAR
  Short gas stations absorb a little PAR

## Slide 24: Improvements - Structure Value
Structure value improvements largely dependent on:
  Better estimates of structures’ square foot
    Fewer generics
  Better estimate of basement status
  Indexed price levels
  Depreciation

## Slide 25: Improvements - Structure Value
NSI1 structure value assumed generic multi-family square feet
RES1 value was split equally among all structures
  Regardless of number of stories or basement status

## Slide 26: Improvements - Structure Value
NSI2 adjusts for:
  Locality (as did NSI 1)
  Depreciation (median year built)
RES1s also adjusted for
  Number of stories
  Basement
  Quality (Block Group median income ratio)

## Slide 27: Improvements - Structure Value
Square foot = Footprint area * number of stories
RES1:
  Footprints and number of stories are determined by
    Year built
    Census Region
Non-RES1:
  Microsoft, and/or,
  Generic & number of employees estimates

## Slide 28: Improvements - Structure Value
NSI2 simply multiplies the estimated SqFt by the determined $/SqFt

## Slide 29: Improvements – FIRM Map Flood Zone
If in a V-Zone
  More likely to have pier/pile foundation type
  More likely to have high foundation height
Otherwise
  Assume the HAZUS A-Zone distribution of type and height (pre/post FIRM)
Also, kept as a field for informational purposes
X Zone
D Zone
A Zone
V Zone

## Slide 30: Limitations
NSI2 methodology relies on wider array of datasets than NSI1
Inaccuracies/misalignments between these can result in inaccurate structure level data
  Structure Footprints
  RES4, RES5, RES6 population assignment
  “Split” structures
    CoreLogic data inconsistently differentiating single structures vs developments

## Slide 31: Limitations - Structure Footprints
Microsoft footprints do not always accurately capture structures
  Large, multi-story structures/complexes worst offenders
  Relatively common in heavily urban or industrial areas
  Leads to inaccurate square footage and value, can lead to inaccurate number of stories
Structures are sometimes associated with the wrong footprint (e.g. RES2 to large commercial structure footprint)

## Slide 32: Limitations - Structure Footprints
Incomplete footprint coverage in parcel result in incorrectly stacked structures
False positive or inaccurate footprints can result in inaccurate square footage, value assignment

## Slide 33: Limitations - RES4, RES5, & RES6 Population Assignment
RES4, RES5, and RES6 structures taken from ESRI data rather that CoreLogic
Population assignment by employee count rather than residential units
Missing population
  Now treated similar to e.g. customers at COM1’s

## Slide 34: Limitations - “Split” Structures
CoreLogic data sometimes reports large developments as single, RES1 classified structure
Results in individual RES1 structures with hundreds of people assigned
Current approach identifies structures, splits them into sub-structures based on maximum population per housing unit
  These split structures are marked “S” in the “stacked” field
  Structures would need to be moved by modelers as appropriate

## Slide 35: State Level Comparisons: Hawaii
NSI 1
NSI 2
Has not been updated to reflect CL based data

## Slide 36: State Level Comparisons: Virginia
NSI 1
NSI 2
Has not been updated to reflect CL based data

## Slide 37: Model Result Comparisons
Has not been updated to reflect CL based data